## Slide 1: A DSP-based Bunker Cache Co-Processor
Sp2021 ECE757 Shuai Zhang

## Slide 2: Bunker Cache
An approximate cache access method
Fetch neighbor row instead of precise row
Exploit spatial redundancy of images
Requires compiler / ISA support
Automate parameter generation?
J. S. Miguel et al, 2016

## Slide 3: Fourier Transform (FT)
Decompose time domain signal to frequency domain (or reverse, same math!)
Very common place in audio / image processing
  (before being taken over by ML)
Can be generalized into discrete signal and 2D
  Discrete: digital, not continuous
  2D: image !
  Discrete Fourier Transform (DFT)
Can be calculated very fast
  Fast Fourier Transform (FFT)

## Slide 4: FFT can extract image dimension (kind of )
Observation: FFT on a row-major flattened image have peak on multiples its height, vice versa
510 x 340 (W x H)
340

## Slide 5: Possible Structure
The co-processor probes on data bus from disk to memory
  probe for continuous address access.
    If the burst length is more than a certain number, store the FFT result
    If the burst length is no more than the number, AKA, the address jumped to another location, reset
Store all calculated stride parameters in a small cache
index by the address of image
E.g. Image head @ 0x1000_0000
  tail @ 0x1001_0000
  then index is 4’b1000

## Slide 6: Quick Proof-of-Concept Demo

## Slide 7: Major problems (and possible solution)
1. low Resilient to column shift
  Perhaps not a very big issue in ML?
2. Power cost
  ~0.1W @ 50MHz clk
3. some delay (~10K cycle)
  Still tiny compared to IO
4. “cheating image”
  e.g. A zebra, zebra crossing, etc
  No really good solution

## Slide 8: Possible Future Plans
1. use real floating point instead of block floating point
2. better filtering